## Slide 1: Imbalance Prices
Angus Fairbairn
Market Analyst
7 October 2020
Angus Fairbairn
Market Analyst
Notes: This presentation is going to take you through the basics of imbalance pricing – the principles behind the pricing arrangements, the key terminology and an overview of how the prices are calculated and applied.
Unapologetic Beginner’s Guide – will provide links at end to further detail.

## Slide 2: What you’ll take away
Imbalance Prices:
  When are Imbalance Prices used?
  What does Short and Long mean?
  Why are they so important?
  How are they calculated?
  Price calculation example.

## Slide 3: Energy Imbalance Settlement
Elexon accounts for mismatches between BSC Trading Parties’ contracted and metered positions
  Parties notify energy contracts
  Metered volumes collected
  Difference is the Party’s imbalance volume
Imbalance volumes settled at ‘cash-out’ prices, ‘imbalance’ prices or ‘system’ prices
Notes: To recap from this mornings imbalance settlement presentation…
The Process occurs as follows: the parties notify their energy contracts…
The imbalance volumes are then settled at …

## Slide 4: ‘Long’ or ‘Short’ terminology
  Is paid for the ‘surplus’ imbalance at Imbalance Price
  For a Generator: Volume generated > Volume sold
  For a Supplier: Volume consumed < Volume bought
  Pays for the ‘deficit’ imbalance at Imbalance Price
  For a Generator: Volume generated < Volume sold
  For a Supplier: Volume consumed > Volume bought
Short Party
Long Party
Notes: During that presentation, I will often refer to short or long, refereeing either to Parties or system. Let’s get Imbalance Settlement terminology right… Could be different to trading terminologies.
When a party is long (‘surplus’ of energy) the price calculation is based on actions taken by National Grid to reduce generation or increase demand which is a BID
When a party is short (so there's a deficit of energy) then National Grid takes actions to increase generation or reduce demand which is an OFFER

## Slide 5: ‘Long’ or ‘Short’ terminology
  Consumption > generation
  National Grid takes actions to increase the level of energy on the system (Offers)
  Generation > consumption
  National Grid takes actions to reduce the level of energy on the system (Bids)
5
Short System
Long System
Notes: During that presentation, I will often refer to short or long, refereeing either to Parties or system. Let’s get Imbalance Settlement terminology right… Could be different to trading terminologies.
When a party is long (‘surplus’ of energy) the price calculation is based on actions taken by National Grid to reduce generation or increase demand which is a BID
When a party is short (so there's a deficit of energy) then National Grid takes actions to increase generation or reduce demand which is an OFFER

## Slide 6: When are they applied - Long Party example
Bilateral Contract | 75 MWh
Generation volume | 100 MWh
Generating more than the contracted volume…
MWh
Bilaterally contracted
Actually generated
Bilateral contract | 75 MWh
Notes: This is an example illustrating when a party is long. So the party have Bilateral contract of 75 MWhs (hence they’ve sold 75 MWh) but they’ve generation 100MWh so here generation is more than what they have sold. Hence there will be a surplus of energy left over after the trading takes place

## Slide 7: When are they applied - Long Party example
Long imbalance position | 25 MWh
Energy Imbalance Cashflow | +25 MWh * Imbalance Price
Long imbalance position | 25 MWh
Generating more than the contracted volume…
MWh
Imbalance Volume
‘surplus’
Bilateral contract | 75 MWh
Generation volume | 100 MWh
Notes: This surplus of energy is 25 MWhs, which will be sold at the Imbalance Price. So 25 multiplied by the Imbalance Price

## Slide 8: When they are applied - Short Party example
Bilateral Contract | 75 MWh
Generation volume | 75 MWh
Generating less than the contracted volume…
MWh
Bilaterally contracted
Actually generated
Bilateral contract | 100 MWh
Notes: This example is illustrating when a party is short. So here the party has a bilateral contract of 100 MWh (essentially sold 100MWh) But they’ve generated only 75 MWhs
So there is a deficit of energy on the system and hence the party is short

## Slide 9: When they are applied - Short Party example
Long imbalance position | 25 MWh
Energy Imbalance Cashflow | -25 MWh * Imbalance Price
Short imbalance position | -25 MWh
Generating less than the contracted volume…
MWh
Imbalance Volume
‘deficit’
Bilateral contract | 100 MWh
Generation volume | 75 MWh
Notes: The deficit of energy is -25 MWh which the party will need to pay for at the Imbalance Price
The price to paid will be -25 MWh multiplied by the Imbalance Price at that particular settlement period

## Slide 10: Why do we have Imbalance Cashflow?
The energy deficit is still used by customers
The energy has to be produced from a different source
The Party must pay a fair price
The energy surplus is still generated
The energy is used by end consumers
The Party must be paid a fair price
Imbalance Volume
‘surplus’
Imbalance Volume
‘deficit’
The Imbalance Price represents the cost of this energy

## Slide 11: Why are Imbalance Prices important?
Chart: Imbalance Prices on 4 March 2020
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
Imbalance Price (£/MWh) | 42 | 8.1 | 42 | 42 | 41 | 41 | 41 | 41 | 34.86 | 41 | 39.85 | 20.25 | 20.25 | 47.08 | 21 | 66 | 22.5 | 22.25 | 22.3 | 22.55 | 39.353 | 22.61 | 0 | 0 | 22.8 | 37.35 | 72 | 38.598 | 38.35 | 23.35 | 23.35 | 23.47 | 125 | 125 | 119.14 | 144.14 | 2242.307 | 1708.052 | 23.35 | 0 | 25.05 | 66.5 | 104 | 45 | 50 | 55 | 23.5 | 23.5
£21/MWh
£2,242/MWh

## Slide 12: Why are Imbalance Prices important?
Applying 4 March 2020 Imbalance Prices to our Short Party example:
Settlement Period | 15 | 37
Imbalance Volume | -25MWh | -25MWh
Imbalance Price | £21/MWh | £2,242/MWh
Imbalance Cashflow | -£525 | -£56,050

## Slide 13: Where does the imbalance cashflow go?
Short Parties paid
Long Parties were paid
Left over
£8.9M
£840K
RCRC REDISTRIBUTED
£9.7M
For Settlement Period 37 on 4 March 2020:
Any ‘left over’ money after all the Energy Imbalance Cashflow for a Settlement Period is settled, is either credited or charged to active market participants

## Slide 14: How are they calculated?
Notes: Before I move onto the next section of the presentation does anybody have any questions

## Slide 15: How are they calculated?
We will cover:
  Bids & Offers
  System Vs. Energy balancing actions
  Flagging and Tagging processes (these remove or reprice Bids/Offers accepted by National Grid)
  Simplified Working Example
Notes: In this section of the presentation we will recap the balancing mechanism
We will go through system vs energy balancing actions
The flagging and tagging process
And an example to tie everything together

## Slide 16: The Balancing Mechanism
Imbalance Prices are calculated based on the cost incurred by National Grid to balance the system using the Balancing Mechanism
It is based on the price of Bids and Offers that National Grid accepts for a Settlement Period
Notes: National Grids job is to balance the system using Bids and Offers. The imbalance price is then based on the cost of national grid to do this.

## Slide 17: How are they calculated - Bids and Offers
Used by National Grid to balance the system as part of the Balancing Mechanism
Bids and Offers are a Party’s willingness to deviate from their expected position
Bid
to reduce the level of energy on the system:
Party pays (or paid) to ↓ generation or ↑ demand
Offer
to increase the level of energy on the system: Party paid to ↑ generation or ↓ demand
Notes: During the morning presentation, we mentioned Bids and Offer, they are Parties’ willingness to adjust their levels of output from FPN (Final Physical Notification) at a certain price.
National Grid accepts bids/offers in via Balancing Mechanism to help balance demand and generation on the System prior and in real time.
ELEXON will adjust Parties’ contracted position if they accepts any bids/offers to ensure they are not exposed to imbalance from bids/offers.

## Slide 18: Trans European Replacement Reserves Exchange
Volume of GB need met (VGB)
Volume of GB balancing energy need met by TERRE balancing volumes with a volume (MWh) and the TERRE clearing price (£/MWh)
RR Aggregated Unpriced System Actions (RRAUSS and RRAUSB)
Energy balancing volumes from TERRE that does not meet GB need with a volume (MWh) and a price of £0/MWh.
TERRE actions are accepted in 15 minute blocks and are aggregated and incorporated into the pricing stack
Introduces two new balancing action types to our pricing stack
Notes: During the morning presentation, we mentioned Bids and Offer, they are Parties’ willingness to adjust their levels of output from FPN (Final Physical Notification) at a certain price.
National Grid accepts bids/offers in via Balancing Mechanism to help balance demand and generation on the System prior and in real time.
ELEXON will adjust Parties’ contracted position if they accepts any bids/offers to ensure they are not exposed to imbalance from bids/offers.

## Slide 19: Ranking actions in merit order
Offers
  National Grid pay to increase the level of energy
Bids
  National Grid are paid to decrease the level of energy
  (where the price is negative National Grid Pay)
Rank Offers and Bids separately by price to create our Pricing Stack
£70/MWh
£40/MWh
£100/MWh
£50/MWh
Most expensive
Least expensive
-£40/MWh
£30/MWh
£0/MWh
£10/MWh
Most expensive
Least expensive

## Slide 20: How are they calculated - Energy versus system balancing
Energy balancing actions
System balancing actions
    Actions taken to maintain gross national half-hourly energy balance
    To match Supply with Demand
    Market-driven imbalances
    Costs are reflected in the Imbalance Price
    To manage constraints on the network
    Actions taken to balance the system geographically and/or for shorter term balancing, e.g. frequency control
    Non-market driven imbalances
The SO (National Grid) takes both energy balancing actions and system balancing actions
Only energy balancing actions will be included in the Imbalance Price calculation
Imbalance Prices are calculated based on the price of Bids and Offers that National Grid accept to balance the system.
Notes: Specifically the Imbalance Prices are intended to reflect the costs of balancing imbalances in Party’s energy accounts.
However, National Grid accept actions from Parties to balance the system because of constraints too.
System constraints are caused because the transmission is a physical network with limited capacity. We have a single price zone in GB – so physical constraints are stripped out. Therefore, in addition to balancing the overall levels of supply and demand, National Grid must also balance the use of the network geographically to avoid system faults.
Because the Imbalance Prices are intended to reflect the costs of balancing the overall levels of energy supply and demand, the Main Price calculation seeks to exclude or at least limit the impact of System Actions.
When balancing the system national grid take both system and energy balancing actions. However we do not use all balancing actions in the same way since national grid doesn’t take all balancing actions for the same reasons. Some actions are taken purely to balance the half hourly energy imbalance of the Transmission System. (these are called energy balancing actions) But some actions, system balancing actions are taken for non energy reasons and they are simply taken to manage the system. The purpose of the imbalance price calculation is to remove system balancing as they could distort the imbalance price.

## Slide 21: How are they calculated – Tagging and Flagging
Tagging
Flagging
To prevent some actions from distorting the price
Does not remove volume
Flagged actions may be re-priced
To remove volumes of actions we don’t want in the calculation
Notes: Specifically the Imbalance Prices are intended to reflect the costs of balancing imbalances in Party’s energy accounts.
However, National Grid accept actions from Parties to balance the system because of constraints too.
System constraints are caused because the transmission is a physical network with limited capacity. We have a single price zone in GB – so physical constraints are stripped out. Therefore, in addition to balancing the overall levels of supply and demand, National Grid must also balance the use of the network geographically to avoid system faults.
Because the Imbalance Prices are intended to reflect the costs of balancing the overall levels of energy supply and demand, the Main Price calculation seeks to exclude or at least limit the impact of System Actions.

## Slide 22: How are they calculated – Tagging and Flagging
Tagging
(removes volumes)
Flagging
(prevent distortion)
CADL flagging(De Minimis Acceptance Threshold) – actions less than 15 minutes
DMAT tagging
(De Minimis Acceptance Threshold) – Removing actions less than 1MWh
NIV tagging (Net Imbalance Volume) – to determine overall imbalance
PAR tagging (Price Average Reference) – ‘marginal’ price. Only keep the 1MWh most expensive actions.
SO flagging (System Operator) – physical constraint related actions
STOR Provider flagging (Short Term Operating Response) – actions from STOR plants
Arbitrage tagging – removing actions which wouldn’t have happened in an efficient market
Notes: As well as understanding the difference between energy-balancing actions and system-balancing actions there are some other key parameters used in the Main Price calculation.
At the end of the calculation, a Buy Price Adjustment (BPA) is added when the system is short and the Sell Price Adjustment (SPA) is added when the system is long. Part of BSAD. Reflects long-term bilateral contracts between National Grid and Parties outside the BSC (e.g. to provide reserve generation under STOR or ‘run warm’ under BM Start-Up).
Note that CADL, DMAT and PAR set by the BSC Panel and are the same for each Settlement Period. BPA/SPA set by National Grid for each Settlement Period.

## Slide 23: How are they calculated – Flagging
Flagging
(prevent distortion)
CADL flagging – currently actions less than 10 minutes. Was reduced from 15 minutes 1 April 2019.
SO flagging – physical constraint related actions
STOR Provider flagging – actions from STOR plant
Actions potentially re-priced downwards for the price calculation
Actions potentially re-priced upwards for the price calculation
Notes: As well as understanding the difference between energy-balancing actions and system-balancing actions there are some other key parameters used in the Main Price calculation.
At the end of the calculation, a Buy Price Adjustment (BPA) is added when the system is short and the Sell Price Adjustment (SPA) is added when the system is long. Part of BSAD. Reflects long-term bilateral contracts between National Grid and Parties outside the BSC (e.g. to provide reserve generation under STOR or ‘run warm’ under BM Start-Up).
Note that CADL, DMAT and PAR set by the BSC Panel and are the same for each Settlement Period. BPA/SPA set by National Grid for each Settlement Period.

## Slide 24: SO and CADL flagging
SO and CADL flagged actions are potentially repriced downwards. There are three stages to the flagging:
SO and CADL Flagged actions are initially considered Stage 1 Flagged
Classification assess the price of the Stage 1 flagged action against the price of the most expensive unflagged action
Stage 2 Flagged actions are re-priced as the same price as the most expensive unflagged action – called the replacement price
Flagging
To prevent some actions from distorting the price
Flagged actions may be re-priced
CADL Flagging – actions less than 10 minutes
SO Flagging – physical constraint related actions

## Slide 25: SO and CADL Flagged actions
SO and CADL Flagged actions are initially considered Stage 1 Flagged
Most expensive
Ranked Bids
Ranked Offers
Most expensive
Least expensive
SO Flag
CADL Flag
Stage 1 Flag
Stage 1 Flag

## Slide 26: SO and CADL Flagged actions
Stage 1 Flag
Stage 1 Flag
Classification assess the price of the Stage 1 flagged action against the price of the most expensive unflagged action
    If the Stage 1 Flagged action is less expensive the action loses its flag and keeps its price.
    If the Stage 1 flagged action is more expensive then the action becomes Stage 2 Flagged and loses it price.
Most expensive
Ranked Bids
Ranked Offers
Most expensive
Least expensive
Stage 1 Flag
Stage 1 Flag
After DMAT and Arbitrage tagging
Stage 2 Flag
Flag removed
  Most expensive unflagged action

## Slide 27: SO and CADL Flagged actions
Stage 1 Flag
Stage 1 Flag
    Stage 2 Flagged actions are re-priced as the same price as the most expensive unflagged 1MWh
Most expensive
Ranked Bids
Ranked Offers
Most expensive
Least expensive
Stage 1 Flag
Stage 1 Flag
After DMAT and Arbitrage tagging
Stage 2 Flag
Flag removed
Stage 1 Flag
After NIV tagging
Stage 2 Flag
  Replacement Price
Replacement Price applied

## Slide 28: Price Calculation Example
Notes: Now for the Main Price, which is based on NG balancing actions…

## Slide 29: Price calculation steps
Processes (in order)
Report BOAs and BSAD
System Operator flagging
Emergency flagging
STOR Action flagging
Ranking
CADL flagging
De Minimis tagging
Arbitrage tagging
Classification
NIV tagging
Replacement Price
PAR tagging
Price Calculation (including TLM)
BPA/SPA
Notes: National Grid takes care of the two first steps, removing the system-balancing actions, and ELEXON undertakes the remaining stages of the calculation, including….
Emergency Instructions can feed in as BOAs or be tagged out as system-balancing.
Arbitrage tagging - actions which have no effect on the energy balancing of the system but lead to an overall financial benefit for the System Operator.
NIV tagging: Separate Buy and Sell action stacks which are then netted off, leaving either a net volume of Buy actions or a net volume of Sell actions. This is the Net Imbalance Volume or NIV (Excess of Offers => system short=> NIV negative when and Excess of Bids => system long=> NIV positive).

## Slide 30: 1. Receive all balancing actions
1
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
50 MWh at £100/MWh
OFFER
20 MWh at £95/MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
BID
-0.05 MWh at £40/MWh
OFFER
20 MWh at £1,000/MWh
Accepted Bids and Offers
Balancing Services Adjustment Actions (BSAA, actions taken outside the Balancing Mechanism)
Demand Control volumes (priced at Value of Lost Load, £6,000/MWh)
Notes: Value of Lost Load (VoLL) is an administrative value to reflect customers security of supply (ie the ‘price of disconnections’). It is currently set at £3,000/MWh
Supplementary balancing reserve (SBR) and DSBR would also be included at VoLL

## Slide 31: 2. Rank the actions
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
50 MWh at £100/MWh
OFFER
50 MWh at £95/MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
BID
-0.05 MWh at £40/MWh
Offers and Bids are separately ranked from the least to the most expensive
Least expensive
Least expensive
Most expensive
Most expensive
Offer stack
Bid stack
OFFER
20 MWh at £1,000/MWh

## Slide 32: 3. Remove De Minimis and Arbitraged actions
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
50 MWh at £100/MWh
OFFER
50 MWh at £95/MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
BID
-0.05 MWh at £40/MWh
OFFER
20 MWh at £1,000/MWh
Less than De Minimis Acceptance Threshold (DMAT) (0.1 MWh)
*please note April 2019 change
De Minimis and arbitrage actions are ‘tagged’ and removed from the stack

## Slide 33: 4. NIV Tagging
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
50 MWh at £100/MWh
OFFER
20 MWh at £95/MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
= -60 MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
590 MWh
Minus
60 MWh
= 590 MWh
The smaller stack of Bids is subtracted from the most expensive Offers
OFFER
20 MWh at £1,000/MWh
10
NIV = Volume of Offers – Volume of Bids
= 590MWh – 60MWh
= 530MWh
Notes: To determine the overall imbalance

## Slide 34: 5. NIV Tagging
NIV = 530 MWh
Where NIV > 0 then the System is SHORT (More Offers than Bids)
Where NIV < 0 then the System is LONG (More Bids than Offers)
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
10 MWh at £100/MWh
OFFER
20 MWh at £95/MWh

## Slide 35: 6. Flagging and the Replacement Price
Most expensive unflagged action – ie ‘pure energy action’
Replacement Price (£95/MWh)
(set by RPAR, the most expensive 1MWh of unflagged actions)
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
10 MWh at £100/MWh
OFFER
20 MWh at £95/MWh
SO FLAGGED OFFER
10 MWh at £100/MWh
95
SO FLAGGED OFFER
250 MWh at £55/MWh
UNFLAGGED OFFER
250 MWh at £55/MWh
UNFLAGGED OFFER
10 MWh at £95/MWh
Notes: Flagged actions are potentially system balancing – but still part of the NIV
SO flagging for locational constraint
Only want to re-price flagged actions where they would distort the price

## Slide 36: 7. PAR Tagging and final price calculation
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
10 MWh at £95/MWh
= PAR: 1 MWh
1
Imbalance Price is the volume weighted average price of the remaining actions
Adjusted for Transmission Losses – TLM (except for BSAAs)
Plus the Buy Price Price Adjuster (BPA) or Sell Price Price Adjuster (SPA)
OFFER
20 MWh at £95/MWh
Notes: Back to our simple example

## Slide 37: Where to find out more

## Slide 38: Want to know more?
https://www.elexon.co.uk/operations-settlement/balancing-and-settlement/imbalance-pricing/
Notes: For anyone who wants to get into the detail of the calculation, we publish a comprehensive overview on our website. This also contains links to the actual calculations and rules in the BSC.

## Slide 39: System Price Analysis Report (SPAR)
https://www.elexon.co.uk/data/key-data-reports/system-prices-analysis-report/

## Slide 40: Still want to know more?
Balancing Mechanism Reporting Service – BMRS (www.bmreports.com)
  Live reporting – prices within 15 mins of end of Settlement Period
  Indicative prices as may not include all BSAD/BSAA data
  De-rated Margin and Loss of Load Probabilities (LoLPs)
Elexon Portal (www.elexonportal.co.uk)
  Historic prices back to 2001 (‘Best View Prices’ spreadsheet)
  Published at D+1 and updated at each Settlement Run
  Dynamic Loss of Load Probability (LoLP) data

## Slide 41: BMRS website (www.bmreports.com)
INDICATIVE ONLY AND SUBJECT TO CHANGE POST PUBLICATION
Not amended retrospectively

## Slide 42: Angus.Fairbairn@elexon.co.uk
Elexon
7 October 2020