## Slide 1: Imbalance Settlement
David Thomas
Delivery Lead
7 October 2020

## Slide 2: Agenda
In this session, we will cover:
Core Principles of Imbalance Settlement
Contracts and Trading
Collection and Allocation of Meter Reads
Electricity Balancing Mechanism
Imbalance Volume, Price and Charges
BSC Credit Cover and further information

## Slide 3: Core Principles of Imbalance Settlement

## Slide 4: National Grid and Elexon
Grid Code (GC)
Physical Balancing
Balancing physical Generation and Demand on the Network
Balancing and Settlement Code (BSC)
Imbalance Settlement
Calculates imbalances and charges/pays Parties accordingly

## Slide 5: Transmission Network

## Slide 6: Distribution Network
North Scotland
South Scotland
Northern
North Western
Yorkshire
Merseyside & North Wales
East Midlands
South Wales
Midlands
South Western
Southern
Eastern
South Eastern
London

## Slide 7: Distribution Network
_P
_N
_F
_G
_M
_D
_B
_K
_E
_L
_H
_A
_J
_C

## Slide 8: Introduction – Settlement Data
What are Settlement Periods?
  Standard time format used in Settlement (i.e. volumes are per Settlement Period)
  30 minute period, also known as half-hour (HH)
  48 Settlement Periods in a day (excluding clock change days which have 46/50)
Volume (MWh)

## Slide 9: Concept of Imbalance
National Grid Balancing Mechanism
Parties notify contract volumes to Elexon
Metered volumes collected and sent to ELEXON
Difference between metered and contracted volumes is Party’s imbalance
Imbalance volumes settled at Imbalance Price
Settlement Period (SP)
Elexon accounts and settles mismatches between
BSC Parties contracted and metered positions

## Slide 10: Contracts and Trading

## Slide 11: Energy Contracts
Elexon capture the contracted volumes from Generators and Suppliers to see
what they have bought or sold to try and balance their position
Since November 2017, Parties can notify ELEXON of contracts anytime up to the start of a Settlement Period
Parties notify contract volumes to ELEXON
Settlement Period (SP)
Gate Closure
1 hour before start of Settlement Period
Submission Deadline
Before start of Settlement Period
1 HR
Parties notify
contract volumes
to ELEXON

## Slide 12: Bilateral Contracts
An energy contract is a bilateral contract between Generator and Supplier
Submitted to ELEXON by:
    Dedicated ‘High Grade’ Communications Line
    ‘Low Grade’ web connection
    ‘ECVAA Web Service’ (EWS)

## Slide 13: Contract Notifications
Trading Party 1 Account
Trading Party 2 Account
Energy Contract Volume Notification Agent (ECVNA)
Elexon Systems
Bilateral Contract
Contract Volume Details
Contract Volume Details

## Slide 14: Contract Notifications
Trading Party 1 Account
Trading Party 2 Account
Elexon Systems
Contract Volume Details
Contract Volume Details
Power Exchange

## Slide 15: National Grid and Elexon
Forward Contract Report
Released 4 times per day
Reference: ECVAA-I022
Provides forward view of Settlement Period contract position for all acknowledged energy contracts
Covers 7 Settlement Days following the Settlement Day on which the report is provided
End of Day Report
Released ~2am D+1
Reference: ECVAA-I014
Summarises the energy contract volumes (ECVNs) and metered volume reallocations (MVRNs) for the last Settlement Day
Provides period and cumulative indebtedness data and identifies Parties in Credit Default

## Slide 16: Metering Collection and Allocation

## Slide 17: Collection of metered data
Grid Supply Points
(GSPs)
Suppliers
Generators
Imbalance Settlement
Elexon systems capture metered data to understand who consumed or generated energy during the Settlement Period

## Slide 18: Balancing Mechanism Units (BMUs)
T_NAME-1
I_IBG_NAME
I_IBD_NAME
Meter Point
Sites that are directly connected to the Transmission System
Meter Point
Sites that are embedded into the Distribution System
Meter Point
Meter Point
Sites that are related to an Interconnector
V_NAME-1
Meter Point
Sites that are within Supplier BM Units and offer flexibility services
E_NAME-1

## Slide 19: Supplier Base BM Units
Suppliers have 14 BM Units as default – one per GSP Group
2__CNAME000
Aggregated data from meter points
All Meter points in GSP Group C
2__BNAME000
Aggregated data from meter points
All Meter points in GSP Group B
Aggregated data from meter points
2__ANAME000
All Meter points in GSP Group A

## Slide 20: Metered Energy Volumes
Grid Supply Points
(GSPs)
Suppliers
Generators
T_NAME-1
Aggregated data from meter points
Aggregated data from meter points
Meter Point
Meter Point
Meter Point
E_NAME-1
2__BNAME000
2__ANAME000

## Slide 21: Party Accounts
Aggregated data from meter points
Aggregated data from meter points
Meter Point
Meter Point
BSC Party
Production Account
Consumption Account
E_BMU
T_BMU
2__ABMU
2__BBMU
…

## Slide 22: Metered Volume Reallocation Notification (MVRN)
BSC Party 1
Production Account
Consumption Account
BSC Party 2
Production Account
E_BMU
T_BMU
2__ABMU
2__BBMU
Move a fixed MWh volume or % of volume, to 1 or more Parties
From P Account to P Account, or from C Account to C Account
MVRN

## Slide 23: Electricity Balancing Mechanism

## Slide 24: What is the Balancing Mechanism?
National Grid provides data on actions taken to balance the System

## Slide 25: Forecast National Demand
National Grid’s demand forecast indicates how much energy will be needed for each HH
They can then compare this to the generation planned to be dispatched

## Slide 26: Physical Notifications (PN)
Initial Physical Notification (IPN)
  Expected operating levels throughout the whole day for each BM Unit
  Submitted by 11.00 day ahead
Final Physical Notification (FPN)
  Expected operating level for Settlement Period for each BM Unit
  Submitted by Gate Closure

## Slide 27: Bids and Offers
Offer to increase energy to the system
  Increase generation or decrease demand
Bid to remove energy from the system
  Decrease generation or increase demand
Offer
Bid
Bids and Offers are a BSC Party’s willingness to operate the BM Unit differently to their FPN.

## Slide 28: Bid/Offer Submission
A Bid/Offer submission from a Generator with an FPN of 300MW would look like this…
Contracted Sales
£50/MWh
£30/MWh
-£15/MWh
-£20/MWh
FPN
Offers
Bids
Time
Energy
500MW
400MW
300MW
200MW
100MW

## Slide 29: Bid/Offer Submission
National Grid accept an Offer, so the Generator increases their generation output to 450MW…
Contracted Sales
£50/MWh
£30/MWh
-£15/MWh
-£20/MWh
FPN
Offers
Bids
Time
Energy
500MW
400MW
300MW
200MW
100MW
50MW @ £50/MWh
100MW @ £30/MWh

## Slide 30: Bid/Offer Submission
National Grid accept a Bid, so the Generator decreases their generation output to 220MW…
Contracted Sales
£50/MWh
£30/MWh
-£15/MWh
-£20/MWh
FPN
Offers
Bids
Time
Energy
500MW
400MW
300MW
200MW
100MW
80MW @ -£15/MWh

## Slide 31: Imbalance Volume and Price

## Slide 32: Imbalance Volume
Elexon takes the Imbalance Volume and multiplies this by the Imbalance Price to calculate the Imbalance Charge
Imbalance Volume
Metered Volumes
Accepted Balancing Actions
Contracted Volumes

## Slide 33: Imbalance Position
  Is paid for the ‘surplus’ imbalance at System Price
  For a Generator: Volume generated > Volume sold
  For a Supplier: Volume consumed < Volume bought
PARTY IS LONG
  Pays for the ‘deficit’ imbalance at System Price
  For a Generator: Volume generated < Volume sold
  For a Supplier: Volume consumed > Volume bought
PARTY IS SHORT

## Slide 34: Imbalance Position Example
Contract to sell 100MWh
Contract to buy
200MWh
Power stations generated 90MWh in total
Total customers consumption 180 MWh
BSC Party
Contracted Volumes
Metered Volumes
Imbalance Volumes
Account Level
BM Unit Level
+10 MWh
- 10MWh
+ 20MWh

## Slide 35: Single Imbalance Price
1
OFFER 250 MWh at £45/MWh
1
OFFER 250 MWh at £55/MWh
1
OFFER 50 MWh at £100/MWh
1
OFFER 20 MWh at £95/MWh
1
BID 300 MWh at £35/MWh
1
BID 30 MWh at £20/MWh
1
BID 0.5 MWh at £40/MWh
£/MWh

## Slide 36: Imbalance Charge
Balancing Actions taken by National Grid are included in the calculation of the imbalance price
Elexon calculate a single imbalance price for a given half hour
Imbalance Volume
Imbalance Price
Imbalance Charge
X
=
Imbalance Charge

## Slide 37: Trading Charges and Credit Cover

## Slide 38: Your Invoice – Trading Charges
Residual Cashflow Reallocation Cashflow (RCRC)
Energy Imbalance Cashflow
BM Unit Cashflow
BM Unit Non-Delivery Charge

## Slide 39: Data Reconciliation
?
+5 WD
+18 WD...
+290 WD
(≈14 months)
Settlement Day
What’s a Settlement Run?
A ‘snapshot’ of available data for a day after the event
With each Settlement Run, the accuracy of the data should improve

## Slide 40: Settlement Timetable
Settlement Calendar
Available on the ELEXON Portal (www.elexonportal.co.uk)
Settlement Run | ID | Working Days | NHH Performance | HH Performance
Interim Information Run | II | 5 | N/A | 99%
Initial Settlement Run | SF | 18 | N/A | 99%
1st Reconciliation Run | R1 | 37 | 30% | 99%
2nd Reconciliation Run | R2 | 82 | 60% | 99%
3rd Reconciliation Run | R3 | 152 | 80% | 99%
Final Reconciliation Run | RF | 290 | 97% | 99%
Dispute Reconciliation Run | DF | 595 | N/A | N/A
For information only
Billable

## Slide 41: Concept of Imbalance
Elexon capture the contracted volumes from Generators and Suppliers so we can see what they have bought or sold to try and balance their position
Settlement Period takes place
Elexon systems capture metered data to understand who consumed or generated energy during the Settlement Period
National Grid provides data on actions taken to balance the System
Elexon calculates the Imbalance Volume, multiplies this by the Imbalance Price, to calculate the Imbalance Charge
BSC Parties will receive invoices for their Trading Charges

## Slide 42: BSC Credit Cover
80%
90%
100%
Credit Cover
Level 1 Default
Level 2 Default
29 days Energy Indebtedness
Due to the settlement run timetable, an invoice for a settlement day is paid, on average, 29 calendar days after it occurs
Elexon therefore ask parties to lodge collateral to cover 29 calendar days of indebtedness

## Slide 43: David.Thomas@elexon.co.uk
Elexon
7 October 2020

## Slide 44: Imbalance Prices
Angus Fairbairn
Market Analyst
7 October 2020
Angus Fairbairn
Market Analyst
Notes: This presentation is going to take you through the basics of imbalance pricing – the principles behind the pricing arrangements, the key terminology and an overview of how the prices are calculated and applied.
Unapologetic Beginner’s Guide – will provide links at end to further detail.

## Slide 45: What you’ll take away
Imbalance Prices:
  When are Imbalance Prices used?
  What does Short and Long mean?
  Why are they so important?
  How are they calculated?
  Price calculation example.

## Slide 46: Energy Imbalance Settlement
Elexon accounts for mismatches between BSC Trading Parties’ contracted and metered positions
  Parties notify energy contracts
  Metered volumes collected
  Difference is the Party’s imbalance volume
Imbalance volumes settled at ‘cash-out’ prices, ‘imbalance’ prices or ‘system’ prices
Notes: To recap from this mornings imbalance settlement presentation…
The Process occurs as follows: the parties notify their energy contracts…
The imbalance volumes are then settled at …

## Slide 47: ‘Long’ or ‘Short’ terminology
  Is paid for the ‘surplus’ imbalance at Imbalance Price
  For a Generator: Volume generated > Volume sold
  For a Supplier: Volume consumed < Volume bought
  Pays for the ‘deficit’ imbalance at Imbalance Price
  For a Generator: Volume generated < Volume sold
  For a Supplier: Volume consumed > Volume bought
Short Party
Long Party
Notes: During that presentation, I will often refer to short or long, refereeing either to Parties or system. Let’s get Imbalance Settlement terminology right… Could be different to trading terminologies.
When a party is long (‘surplus’ of energy) the price calculation is based on actions taken by National Grid to reduce generation or increase demand which is a BID
When a party is short (so there's a deficit of energy) then National Grid takes actions to increase generation or reduce demand which is an OFFER

## Slide 48: ‘Long’ or ‘Short’ terminology
  Consumption > generation
  National Grid takes actions to increase the level of energy on the system (Offers)
  Generation > consumption
  National Grid takes actions to reduce the level of energy on the system (Bids)
48
Short System
Long System
Notes: During that presentation, I will often refer to short or long, refereeing either to Parties or system. Let’s get Imbalance Settlement terminology right… Could be different to trading terminologies.
When a party is long (‘surplus’ of energy) the price calculation is based on actions taken by National Grid to reduce generation or increase demand which is a BID
When a party is short (so there's a deficit of energy) then National Grid takes actions to increase generation or reduce demand which is an OFFER

## Slide 49: When are they applied - Long Party example
Bilateral Contract | 75 MWh
Generation volume | 100 MWh
Generating more than the contracted volume…
MWh
Bilaterally contracted
Actually generated
Bilateral contract | 75 MWh
Notes: This is an example illustrating when a party is long. So the party have Bilateral contract of 75 MWhs (hence they’ve sold 75 MWh) but they’ve generation 100MWh so here generation is more than what they have sold. Hence there will be a surplus of energy left over after the trading takes place

## Slide 50: When are they applied - Long Party example
Long imbalance position | 25 MWh
Energy Imbalance Cashflow | +25 MWh * Imbalance Price
Long imbalance position | 25 MWh
Generating more than the contracted volume…
MWh
Imbalance Volume
‘surplus’
Bilateral contract | 75 MWh
Generation volume | 100 MWh
Notes: This surplus of energy is 25 MWhs, which will be sold at the Imbalance Price. So 25 multiplied by the Imbalance Price

## Slide 51: When they are applied - Short Party example
Bilateral Contract | 75 MWh
Generation volume | 75 MWh
Generating less than the contracted volume…
MWh
Bilaterally contracted
Actually generated
Bilateral contract | 100 MWh
Notes: This example is illustrating when a party is short. So here the party has a bilateral contract of 100 MWh (essentially sold 100MWh) But they’ve generated only 75 MWhs
So there is a deficit of energy on the system and hence the party is short

## Slide 52: When they are applied - Short Party example
Long imbalance position | 25 MWh
Energy Imbalance Cashflow | -25 MWh * Imbalance Price
Short imbalance position | -25 MWh
Generating less than the contracted volume…
MWh
Imbalance Volume
‘deficit’
Bilateral contract | 100 MWh
Generation volume | 75 MWh
Notes: The deficit of energy is -25 MWh which the party will need to pay for at the Imbalance Price
The price to paid will be -25 MWh multiplied by the Imbalance Price at that particular settlement period

## Slide 53: Why do we have Imbalance Cashflow?
The energy deficit is still used by customers
The energy has to be produced from a different source
The Party must pay a fair price
The energy surplus is still generated
The energy is used by end consumers
The Party must be paid a fair price
Imbalance Volume
‘surplus’
Imbalance Volume
‘deficit’
The Imbalance Price represents the cost of this energy

## Slide 54: Why are Imbalance Prices important?
Chart: Imbalance Prices on 4 March 2020
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
Imbalance Price (£/MWh) | 42 | 8.1 | 42 | 42 | 41 | 41 | 41 | 41 | 34.86 | 41 | 39.85 | 20.25 | 20.25 | 47.08 | 21 | 66 | 22.5 | 22.25 | 22.3 | 22.55 | 39.353 | 22.61 | 0 | 0 | 22.8 | 37.35 | 72 | 38.598 | 38.35 | 23.35 | 23.35 | 23.47 | 125 | 125 | 119.14 | 144.14 | 2242.307 | 1708.052 | 23.35 | 0 | 25.05 | 66.5 | 104 | 45 | 50 | 55 | 23.5 | 23.5
£21/MWh
£2,242/MWh

## Slide 55: Why are Imbalance Prices important?
Applying 4 March 2020 Imbalance Prices to our Short Party example:
Settlement Period | 15 | 37
Imbalance Volume | -25MWh | -25MWh
Imbalance Price | £21/MWh | £2,242/MWh
Imbalance Cashflow | -£525 | -£56,050

## Slide 56: Where does the imbalance cashflow go?
Short Parties paid
Long Parties were paid
Left over
£8.9M
£840K
RCRC REDISTRIBUTED
£9.7M
For Settlement Period 37 on 4 March 2020:
Any ‘left over’ money after all the Energy Imbalance Cashflow for a Settlement Period is settled, is either credited or charged to active market participants

## Slide 57: How are they calculated?
Notes: Before I move onto the next section of the presentation does anybody have any questions

## Slide 58: How are they calculated?
We will cover:
  Bids & Offers
  System Vs. Energy balancing actions
  Flagging and Tagging processes (these remove or reprice Bids/Offers accepted by National Grid)
  Simplified Working Example
Notes: In this section of the presentation we will recap the balancing mechanism
We will go through system vs energy balancing actions
The flagging and tagging process
And an example to tie everything together

## Slide 59: The Balancing Mechanism
Imbalance Prices are calculated based on the cost incurred by National Grid to balance the system using the Balancing Mechanism
It is based on the price of Bids and Offers that National Grid accepts for a Settlement Period
Notes: National Grids job is to balance the system using Bids and Offers. The imbalance price is then based on the cost of national grid to do this.

## Slide 60: How are they calculated - Bids and Offers
Used by National Grid to balance the system as part of the Balancing Mechanism
Bids and Offers are a Party’s willingness to deviate from their expected position
Bid
to reduce the level of energy on the system:
Party pays (or paid) to ↓ generation or ↑ demand
Offer
to increase the level of energy on the system: Party paid to ↑ generation or ↓ demand
Notes: During the morning presentation, we mentioned Bids and Offer, they are Parties’ willingness to adjust their levels of output from FPN (Final Physical Notification) at a certain price.
National Grid accepts bids/offers in via Balancing Mechanism to help balance demand and generation on the System prior and in real time.
ELEXON will adjust Parties’ contracted position if they accepts any bids/offers to ensure they are not exposed to imbalance from bids/offers.

## Slide 61: Trans European Replacement Reserves Exchange
Volume of GB need met (VGB)
Volume of GB balancing energy need met by TERRE balancing volumes with a volume (MWh) and the TERRE clearing price (£/MWh)
RR Aggregated Unpriced System Actions (RRAUSS and RRAUSB)
Energy balancing volumes from TERRE that does not meet GB need with a volume (MWh) and a price of £0/MWh.
TERRE actions are accepted in 15 minute blocks and are aggregated and incorporated into the pricing stack
Introduces two new balancing action types to our pricing stack
Notes: During the morning presentation, we mentioned Bids and Offer, they are Parties’ willingness to adjust their levels of output from FPN (Final Physical Notification) at a certain price.
National Grid accepts bids/offers in via Balancing Mechanism to help balance demand and generation on the System prior and in real time.
ELEXON will adjust Parties’ contracted position if they accepts any bids/offers to ensure they are not exposed to imbalance from bids/offers.

## Slide 62: Ranking actions in merit order
Offers
  National Grid pay to increase the level of energy
Bids
  National Grid are paid to decrease the level of energy
  (where the price is negative National Grid Pay)
Rank Offers and Bids separately by price to create our Pricing Stack
£70/MWh
£40/MWh
£100/MWh
£50/MWh
Most expensive
Least expensive
-£40/MWh
£30/MWh
£0/MWh
£10/MWh
Most expensive
Least expensive

## Slide 63: How are they calculated - Energy versus system balancing
Energy balancing actions
System balancing actions
    Actions taken to maintain gross national half-hourly energy balance
    To match Supply with Demand
    Market-driven imbalances
    Costs are reflected in the Imbalance Price
    To manage constraints on the network
    Actions taken to balance the system geographically and/or for shorter term balancing, e.g. frequency control
    Non-market driven imbalances
The SO (National Grid) takes both energy balancing actions and system balancing actions
Only energy balancing actions will be included in the Imbalance Price calculation
Imbalance Prices are calculated based on the price of Bids and Offers that National Grid accept to balance the system.
Notes: Specifically the Imbalance Prices are intended to reflect the costs of balancing imbalances in Party’s energy accounts.
However, National Grid accept actions from Parties to balance the system because of constraints too.
System constraints are caused because the transmission is a physical network with limited capacity. We have a single price zone in GB – so physical constraints are stripped out. Therefore, in addition to balancing the overall levels of supply and demand, National Grid must also balance the use of the network geographically to avoid system faults.
Because the Imbalance Prices are intended to reflect the costs of balancing the overall levels of energy supply and demand, the Main Price calculation seeks to exclude or at least limit the impact of System Actions.
When balancing the system national grid take both system and energy balancing actions. However we do not use all balancing actions in the same way since national grid doesn’t take all balancing actions for the same reasons. Some actions are taken purely to balance the half hourly energy imbalance of the Transmission System. (these are called energy balancing actions) But some actions, system balancing actions are taken for non energy reasons and they are simply taken to manage the system. The purpose of the imbalance price calculation is to remove system balancing as they could distort the imbalance price.

## Slide 64: How are they calculated – Tagging and Flagging
Tagging
Flagging
To prevent some actions from distorting the price
Does not remove volume
Flagged actions may be re-priced
To remove volumes of actions we don’t want in the calculation
Notes: Specifically the Imbalance Prices are intended to reflect the costs of balancing imbalances in Party’s energy accounts.
However, National Grid accept actions from Parties to balance the system because of constraints too.
System constraints are caused because the transmission is a physical network with limited capacity. We have a single price zone in GB – so physical constraints are stripped out. Therefore, in addition to balancing the overall levels of supply and demand, National Grid must also balance the use of the network geographically to avoid system faults.
Because the Imbalance Prices are intended to reflect the costs of balancing the overall levels of energy supply and demand, the Main Price calculation seeks to exclude or at least limit the impact of System Actions.

## Slide 65: How are they calculated – Tagging and Flagging
Tagging
(removes volumes)
Flagging
(prevent distortion)
CADL flagging (Continuous Acceptance Duration Limit) – actions less than 15 minutes
DMAT tagging
(De Minimis Acceptance Threshold) – Removing actions less than 0.1MWh
NIV tagging (Net Imbalance Volume) – to determine overall imbalance
PAR tagging (Price Average Reference) – ‘marginal’ price. Only keep the 1MWh most expensive actions.
SO flagging (System Operator) – physical constraint related actions
STOR Provider flagging (Short Term Operating Reserve) – actions from STOR plants
Arbitrage tagging – removing actions which wouldn’t have happened in an efficient market
Notes: As well as understanding the difference between energy-balancing actions and system-balancing actions there are some other key parameters used in the Main Price calculation.
At the end of the calculation, a Buy Price Adjustment (BPA) is added when the system is short and the Sell Price Adjustment (SPA) is added when the system is long. Part of BSAD. Reflects long-term bilateral contracts between National Grid and Parties outside the BSC (e.g. to provide reserve generation under STOR or ‘run warm’ under BM Start-Up).
Note that CADL, DMAT and PAR set by the BSC Panel and are the same for each Settlement Period. BPA/SPA set by National Grid for each Settlement Period.

## Slide 66: How are they calculated – Flagging
Flagging
(prevent distortion)
CADL flagging – currently actions less than 10 minutes. Was reduced from 15 minutes 1 April 2019.
SO flagging – physical constraint related actions
STOR Provider flagging – actions from STOR plant
Actions potentially re-priced downwards for the price calculation
Actions potentially re-priced upwards for the price calculation
Notes: As well as understanding the difference between energy-balancing actions and system-balancing actions there are some other key parameters used in the Main Price calculation.
At the end of the calculation, a Buy Price Adjustment (BPA) is added when the system is short and the Sell Price Adjustment (SPA) is added when the system is long. Part of BSAD. Reflects long-term bilateral contracts between National Grid and Parties outside the BSC (e.g. to provide reserve generation under STOR or ‘run warm’ under BM Start-Up).
Note that CADL, DMAT and PAR set by the BSC Panel and are the same for each Settlement Period. BPA/SPA set by National Grid for each Settlement Period.

## Slide 67: SO and CADL flagging
SO and CADL flagged actions are potentially repriced downwards. There are three stages to the flagging:
SO and CADL Flagged actions are initially considered Stage 1 Flagged
Classification assess the price of the Stage 1 flagged action against the price of the most expensive unflagged action
Stage 2 Flagged actions are re-priced as the same price as the most expensive unflagged action – called the replacement price
Flagging
To prevent some actions from distorting the price
Flagged actions may be re-priced
CADL Flagging – actions less than 10 minutes
SO Flagging – physical constraint related actions

## Slide 68: SO and CADL Flagged actions
SO and CADL Flagged actions are initially considered Stage 1 Flagged
Most expensive
Ranked Bids
Ranked Offers
Most expensive
Least expensive
SO Flag
CADL Flag
Stage 1 Flag
Stage 1 Flag

## Slide 69: SO and CADL Flagged actions
Stage 1 Flag
Stage 1 Flag
Classification assess the price of the Stage 1 flagged action against the price of the most expensive unflagged action
    If the Stage 1 Flagged action is less expensive the action loses its flag and keeps its price.
    If the Stage 1 flagged action is more expensive then the action becomes Stage 2 Flagged and loses it price.
Most expensive
Ranked Bids
Ranked Offers
Most expensive
Least expensive
Stage 1 Flag
Stage 1 Flag
After DMAT and Arbitrage tagging
Stage 2 Flag
Flag removed
  Most expensive unflagged action

## Slide 70: SO and CADL Flagged actions
Stage 1 Flag
Stage 1 Flag
    Stage 2 Flagged actions are re-priced as the same price as the most expensive unflagged 1MWh
Most expensive
Ranked Bids
Ranked Offers
Most expensive
Least expensive
Stage 1 Flag
Stage 1 Flag
After DMAT and Arbitrage tagging
Stage 2 Flag
Flag removed
Stage 1 Flag
After NIV tagging
Stage 2 Flag
  Replacement Price
Replacement Price applied

## Slide 71: Price Calculation Example
Notes: Now for the Main Price, which is based on NG balancing actions…

## Slide 72: Price calculation steps
Processes (in order)
Report BOAs and BSAD
System Operator flagging
Emergency flagging
STOR Action flagging
Ranking
CADL flagging
De Minimis tagging
Arbitrage tagging
Classification
NIV tagging
Replacement Price
PAR tagging
Price Calculation (including TLM)
BPA/SPA
Notes: National Grid takes care of the two first steps, removing the system-balancing actions, and ELEXON undertakes the remaining stages of the calculation, including….
Emergency Instructions can feed in as BOAs or be tagged out as system-balancing.
Arbitrage tagging - actions which have no effect on the energy balancing of the system but lead to an overall financial benefit for the System Operator.
NIV tagging: Separate Buy and Sell action stacks which are then netted off, leaving either a net volume of Buy actions or a net volume of Sell actions. This is the Net Imbalance Volume or NIV (Excess of Offers => system short=> NIV negative when and Excess of Bids => system long=> NIV positive).

## Slide 73: 1. Receive all balancing actions
1
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
50 MWh at £100/MWh
OFFER
20 MWh at £95/MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
BID
-0.05 MWh at £40/MWh
OFFER
20 MWh at £1,000/MWh
Accepted Bids and Offers
Balancing Services Adjustment Actions (BSAA, actions taken outside the Balancing Mechanism)
Demand Control volumes (priced at Value of Lost Load, £6,000/MWh)
Notes: Value of Lost Load (VoLL) is an administrative value to reflect customers security of supply (ie the ‘price of disconnections’). It is currently set at £3,000/MWh
Supplementary balancing reserve (SBR) and DSBR would also be included at VoLL

## Slide 74: 2. Rank the actions
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
50 MWh at £100/MWh
OFFER
50 MWh at £95/MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
BID
-0.05 MWh at £40/MWh
Offers and Bids are separately ranked from the least to the most expensive
Least expensive
Least expensive
Most expensive
Most expensive
Offer stack
Bid stack
OFFER
20 MWh at £1,000/MWh

## Slide 75: 3. Remove De Minimis and Arbitraged actions
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
50 MWh at £100/MWh
OFFER
50 MWh at £95/MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
BID
-0.05 MWh at £40/MWh
OFFER
20 MWh at £1,000/MWh
Less than De Minimis Acceptance Threshold (DMAT) (0.1 MWh)
*please note April 2019 change
De Minimis and arbitrage actions are ‘tagged’ and removed from the stack

## Slide 76: 4. NIV Tagging
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
50 MWh at £100/MWh
OFFER
20 MWh at £95/MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
= -60 MWh
BID
-30 MWh at £35/MWh
BID
-30 MWh at £20/MWh
590 MWh
Minus
60 MWh
= 590 MWh
The smaller stack of Bids is subtracted from the most expensive Offers
OFFER
20 MWh at £1,000/MWh
10
NIV = Volume of Offers – Volume of Bids
= 590MWh – 60MWh
= 530MWh
Notes: To determine the overall imbalance

## Slide 77: 5. NIV Tagging
NIV = 530 MWh
Where NIV > 0 then the System is SHORT (More Offers than Bids)
Where NIV < 0 then the System is LONG (More Bids than Offers)
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
10 MWh at £100/MWh
OFFER
20 MWh at £95/MWh

## Slide 78: 6. Flagging and the Replacement Price
Most expensive unflagged action – ie ‘pure energy action’
Replacement Price (£95/MWh)
(set by RPAR, the most expensive 1MWh of unflagged actions)
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
10 MWh at £100/MWh
OFFER
20 MWh at £95/MWh
SO FLAGGED OFFER
10 MWh at £100/MWh
95
SO FLAGGED OFFER
250 MWh at £55/MWh
UNFLAGGED OFFER
250 MWh at £55/MWh
UNFLAGGED OFFER
10 MWh at £95/MWh
Notes: Flagged actions are potentially system balancing – but still part of the NIV
SO flagging for locational constraint
Only want to re-price flagged actions where they would distort the price

## Slide 79: 7. PAR Tagging and final price calculation
OFFER
250 MWh at £45/MWh
OFFER
250 MWh at £55/MWh
OFFER
10 MWh at £95/MWh
= PAR: 1 MWh
1
Imbalance Price is the volume weighted average price of the remaining actions
Adjusted for Transmission Losses – TLM (except for BSAAs)
Plus the Buy Price Price Adjuster (BPA) or Sell Price Price Adjuster (SPA)
OFFER
20 MWh at £95/MWh
Notes: Back to our simple example

## Slide 80: Where to find out more

## Slide 81: Want to know more?
https://www.elexon.co.uk/operations-settlement/balancing-and-settlement/imbalance-pricing/
Notes: For anyone who wants to get into the detail of the calculation, we publish a comprehensive overview on our website. This also contains links to the actual calculations and rules in the BSC.

## Slide 82: System Price Analysis Report (SPAR)
https://www.elexon.co.uk/data/key-data-reports/system-prices-analysis-report/

## Slide 83: Still want to know more?
Balancing Mechanism Reporting Service – BMRS (www.bmreports.com)
  Live reporting – prices within 15 mins of end of Settlement Period
  Indicative prices as may not include all BSAD/BSAA data
  De-rated Margin and Loss of Load Probabilities (LoLPs)
ELEXON Portal (www.elexonportal.co.uk)
  Historic prices back to 2001 (‘Best View Prices’ spreadsheet)
  Published at D+1 and updated at each Settlement Run
  Dynamic Loss of Load Probability (LoLP) data

## Slide 84: BMRS website (www.bmreports.com)
INDICATIVE ONLY AND SUBJECT TO CHANGE POST PUBLICATION
Not amended retrospectively

## Slide 85: Angus.Fairbairn@elexon.co.uk
Elexon
7 October 2020

## Slide 86: Supplier Volume Allocation (SVA)
Nick Baker
Product Analyst
7 October 2020

## Slide 87: What are we going to cover in this presentation?
What is Supplier Volume Allocation (SVA)?
Types of meters and challenges with Settlement
Suppliers and the Supplier Hub
Non-Half Hourly Settlement
        - Introduction to Profiling
        - What EAC & AAs are, how they are calculated and used
GSP Group Correction Factor (GCF)
Settlement Process

## Slide 88: Imbalance Settlement Recap

## Slide 89: Recap- Concept of Imbalance
Elexon accounts and settles mismatches between BSC Parties contracted and metered positions
Parties notify contract volumes to Elexon
National Grid Balancing Mechanism
Settlement Period (SP)
Difference between metered and contracted volumes is Party’s imbalance
Metered volumes collected and sent to Elexon
Imbalance volumes settled at Imbalance Price

## Slide 90: Recap – What does ‘Imbalance’ mean?
Contracted volumes
Metered volumes
With what a Generator actually produced…
And calculate payments where the two don’t match
Compare what a Generator agreed to sell…
With what a Supplier actually consumed…
And calculate payments where the two don’t match
Compare what a Supplier agreed to buy…

## Slide 91: Introduction to SuppLier Volume AllOCation

## Slide 92: CVA and SVA
Grid Supply Point (GSP)
CVA
Central Volume Allocation
Supplier Volume Allocation
SVA
TRANSMISSION NETWORK
DISTRIBUTION
NETWORK
“THE GRID”
Large Scale Supply
Large Scale Generation
Interconnectors
GSP Groups
Small Scale Supply
Small Scale Generation

## Slide 93: Metering – Half Hourly (HH) Vs Non-Half Hourly (NHH)
HH
Used in all CVA sites
Used in large industrial and commercial SVA sites
Records and stores energy flow volumes per half hour
Easy to use in Settlement
NHH
Used in domestic households
Used in small industrial and commercial sites
Records energy flow continually and requires periodical meter reads
Hard to use in settlement

## Slide 94: Metering – Unmetered Supplies
1% of total Settlement energy
We can manage small, predictable loads as
Unmetered Supplies
Street Lights
Traffic Signals
(e.g. traffic lights, belisha beacons)
Miscellaneous
(e.g. cable cabinets)

## Slide 95: Energy consumption Vs Number of customers
Chart: 
| NHH | HH | UMS
Sales | 134 | 124 | 2.81
Chart: 
| NHH Customers | HH Customers | UMS Customers
Sales | 31011555 | 338137 | 31120
~340k HH customers
~31 million NHH customers
~124 TWh HH consumption
Notes: ****% of consumption figures
31 million
340,000 HH
51.5:47.5:1 (new- Sep-Aug 19-20)
50:49:1 (old)

## Slide 96: Suppliers and the supplier HUB

## Slide 97: What is a Supplier?
SUPPLIER
Owned Generation
Power Purchase Agreements (PPA)
Wholesale Energy Market
Small scale supply
Payment
Billing
Notes: Supplier provides generation to customers
They source their generation from their own gen, ppa’s and the energy trading market Re-coop the costs by billing

## Slide 98: What is a Supplier?
SUPPLIER
Meter Operator
Data Collector
Data Aggregator
THE SUPPLIER HUB
Notes: BSC is just one of many industry codes that puts obligations on Suppliers so appointing Supplier Agents should ensure they remain compliant.
Suppliers have to abide by minimum of 8 codes (MRA, BSC, CUSC etc.)
Must appoint agents in accordance with section J but they are responsible for the actions of their agents.
Section S of the BSC describes the obligations on Suppliers to provide data and ensure that Supplier Agents undertake the requirements defined for them.

## Slide 99: Supplier Agent Roles
Meter Operator (MOP)
Data Collector (DC)
Data Aggregator (DA)
Install and maintain meters
Provide Meter Technical Details to DC
Collect and validate meter reads
Convert reads to annual values
For each Supplier, group consumption together by a number of criteria

## Slide 100: NHH Settlement: Part 1

## Slide 101: NHH Settlement
What about the 30 million customers who only have NHH meters (which are read only a few times a year at most)?
How do we work out what they consumed in a given half hour (Settlement Period)?

## Slide 102: What is a Load Profile?
A Load Profile represents the pattern of daily and annual electricity usage for the average customer in each one of the Profile Classes.
There are a number of variables that affect a demand profile such as:
These are all considered when creating the Load Profiles from the sample consumption data.
Sunset time
Seasons
Day of week
Public Holidays
Temperature
(different for
each GSP group)

## Slide 103: Sample Profiling
1
2
3
Chart: 
Sample customers’ consumption…
Produce profile data: a typical half hourly usage pattern across a year
Apply to all similar customers
Notes: Around 2,000 customers selected and specialist meters installed to monitor consumption.
Produce profile data based on their patterns and usage over a year
Apply to similar customers based on location, usage etc…

## Slide 104: Profile Classes
Profile Class | Type of customer | Description | Example
1 | Domestic | Single/flat electricity rate 24x7 | Domestic premises
2 | Domestic | Multi–rate customers (typically Economy 7 – dual tariff: normal & night) | Domestic premises with switched load capability
3 | Non-Domestic (Commercial) | Single/flat electricity rate 24x7 | Small businesses
4 | Non-Domestic (Commercial) | Multi–rate customers (typically Economy 7 – dual tariff: normal & night) | Small businesses with switched load capability
Notes: Following the implementation of P272, profile data is no longer collected for PC 5-8 (effectively redundant except for a de minimis amount)
Based on when the demand is used not just the volume.

## Slide 105: What is a Load Profile?
A Load Profile represents the pattern of electricity usage by day and by year for the average customer in each one of the four Profile Classes.
Annual
Tuesday
Sunday
Domestic (PC1)
Non - Domestic (PC3)
Notes: We produce seasonal profiles and profiles per day type which reflect British characteristics.
Here are 2 profile shapes, for domestic and non-domestic customer. One annual, One WD and One NWD.
We can see the Sunday ‘lunch’ tradition during noon, the 1st peak of the day compared to the relatively flat shape of commercial (non domestic) sites.
On a Tuesday we can see a typical profile shape for non-domestic customers, like small businesses, expanding along the working hours of the day, while for domestic customers small peak in the morning and then quite flat shape during the day when people are at work.

## Slide 106: NHH Settlement: part 2

## Slide 107: NHH Settlement
How can we aggregate all those consumers’ consumption when their meters are read at different times and cover different periods?
EACs and AAs

## Slide 108: Settlement Consumption
Annualised Advance (AA)
Estimated Annual Consumption (EAC)
Annual rate of consumption derived by extrapolating a meter advance over a year using a profile
Forward looking estimate (weighted average of previous EAC and the new AA)
1st Meter Reading
2nd Meter Reading
AA
EAC
Notes: AA- Advance between two reads used to create a yearly profile. (must be over 6 months for an accurate reflection)
EAC- forward estimate, uses AAs to weight the previous EAC.

## Slide 109: NHH Data Aggregation (NHHDA)
Each Data Aggregator adds up EAC/AAs for customers with same…
Supplier
Profile Class (PC)
GSP Group
Line Loss Factor Class (LLFC)
Standard Settlement Configuration (SSC)
Time Pattern Regime (TPR)
This gives the Data Aggregator the estimated yearly demand for a ‘Super Customer’
Notes: LLFC – how much electricity is lost on the network when it gets to that meter
SSC – type of meter (one rate, two rate etc.)
TPR – how the meter behaves at different times
The super customer can be used as a representative figure for each of the categories.

## Slide 110: NHH Settlement
The role of a Profile is to turn annual values into HH values. To do this we use a profile coefficient.

## Slide 111: NHH Settlement
Meter Advance
AA/EAC
HH estimate
EAC
AA
AA
EAC
EAC
EAC
EAC
AA
EAC
AA
AA
AA
EAC
Period Profile Class Coefficient
X
Aggregated EACs/AAs for Supplier
‘Super Customer’
Notes: *****March 2018 as example
*************Change/simplify
Meter Advance = Meter Reading #2 – Meter Reading #1
AA = Meter Advance / sum(Daily Profile Coeficients)
Use AA and sum(Daily Profile Coefficients) to calculate EAC

## Slide 112: Applying the Period Profile Class Coefficient
1
2
2
Customers of Supplier X Limited…
GSP Group _C
Aggregated annual
consumption of
2,000,000 MWh
Profile Class 1
LLF Class 100
SSC 0393
Notes: Annual consumption for all customers grouped into these specifics is aggregated

## Slide 113: Applying the Period Profile Class Coefficient
3
Settlement Period 14:30 to 15:00 on 17 July 2020
Period Profile Class Coefficient (PPCC) = 0.00006
4
Aggregated annual
consumption of
2,000,000 MWh
X
Period Profile Class Coefficient (PPCC) of 0.00006
=
customers are estimated to have used 120MWh during this Settlement Period
Notes: And multiplied by the profile co-efficient for a given settlement period.
This provides an estimate to a supplier how much energy these customers will use.

## Slide 114: GSP Group Correction

## Slide 115: Grid Supply Point (GSP) Groups
14 host Distribution Networks take energy from the Transmission Network at defined Grid Supply Points.
These networks are also known as GSP Groups.
North Scotland
South Scotland
Northern
North Western
Yorkshire
Merseyside & North Wales
East Midlands
South Wales
Midlands
South Western
Southern
Eastern
South Eastern
London

## Slide 116: GSP Group take – top down and bottom up
What goes into the distribution region

## Slide 117: GSP Group Correction
Using GSP meter reads, we work out what energy enters (or leaves) each Distribution Network per Settlement Period. This is called the Group Take.
Any errors are effectively ‘smeared’ across Suppliers according to their market shares in that GSP Group and Settlement Period.
GSP Group Correction Factors scale Suppliers’ volumes up or down, so that the total of the corrected volumes equals the GSP Group Take.

## Slide 118: GSP Group Correction
0
200
400
600
800
1000
1200
1400
1600
1800
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
41
42
43
44
45
46
47
48
MWh
Settlement Period
Profile Build Up - Uncorrected
HH
Unmetered
PC4
PC3
PC2
PC1
Group Take

## Slide 119: GSP Group Correction Factors

## Slide 120: GSP Group Correction- What is it correcting for?
There are two main potential sources of error:
Volume error
Some examples:
Large EACs and AAs
Undetected theft
Profiling error
Some examples:
Sampling errors
National profiles applied to regional GSP Groups
Special days e.g Easter and Christmas

## Slide 121: Settlement Process

## Slide 122: SVA Settlement process

## Slide 123: Future SVA Settlement process changes?
Ofgem’s Significant Code Review – Electricity Settlement Reform (https://www.ofgem.gov.uk/electricity/retail-market/market-review-and-reform/smarter-markets-programme/electricity-settlement-reform)
Market-wide HH Settlement

## Slide 124: Settlement
Settlement Invoice
Energy Contracts
Credited Energy
BSC Party
Production Account
Consumption Account
E_BMU
T_BMU
2_ABMU
2_BBMU
Aggregated data from meter points
Aggregated data from meter points
Meter Point
Meter Point
Notes: Invoice sent daily if <£500, otherwise wait until reach £500 or quarter
Need to balance each account separately

## Slide 125: nick.baker@elexon.co.uk
020 7380 4337
ANY QUESTIONS?